## Slide 1: New Mexico 911 Program
Resolving NM911 Errors
New Mexico APCO Conference
Farmington, May 2025

## Slide 2: What is EDAC’s Role?
Monthly Tasks
  GIS Data assessment and reporting
  Technical support to Data Providers and PSAPs
  Aggregate statewide NM911 Master Database
  Assisting data providers with corrections
Quarterly Tasks
  MSAG-ALI-GIS data comparison, and reporting
  Assisting data providers/PSAPs with corrections

## Slide 3: GIS Data Upload Status as of April 2025
NM911 GIS Data Status Dashboard https://nm911-hub.maps.arcgis.com
Notes: https://nmdfa911.maps.arcgis.com/apps/dashboards/17138aaca5e540ada8411bc4c6fc42f9

## Slide 4: GIS Data Model (Current/Legacy)
Required Layers
  Address Points
  Road Centerlines
  Addressing/Administrative Boundary – Provisioning Boundary*
  Emergency Service Zone (ESZ) Boundary**
  Public Safety Answering Point (PSAP) Boundary
Optional Layers
  Public Facilities, Community Boundary, Hydrology, Railroads, Mile Markers, Bridges
* Provisioning boundary will be used if available. Required for Next Gen 9-1-1
** Not all data providers maintain or utilize ESZs

## Slide 5: NM911 GIS Data Assessment Workflow
Collection
Conversion
Processing/ Assessment
Reporting
Aggregating & Delivery

## Slide 6
Collection | 
Conversion | 
Processing/ Assessment | 
Reporting | 
Aggregating & Publishing | 
Email notification to GIS POCs
Data Upload to the NM911 Data Portal
Notify GIS POCs & Receive Feedback
Create a version of NM911 geodatabase for each GIS data provider
Check for valid data attributes
Spatial and Tabular checks
Topology Checks
Data Reviewer Checks
Create Fishbone lines
Generate Monthly Data Assessment Reports, Quarterly MSAG/ALI/GIS Comparison Reports and corresponding error geodatabases
Upload reports and error geodatabases to the NM911 Data Portal
Aggregate address and road data to create a statewide master datasets
Check data formats
Update monthly error statistics for each data provider on the NM911 GIS Dashboard
Deliver to NM DFA for PSAP updates & publish to RGIS data clearinghouse for public access
If invalid
If invalid
Technical Assistance with Data upload, Understanding reports and error data & Data Correction
Crosswalk data to NM911 GIS Data Model
MSAG data download from Intrado (quarterly)
ALI data download from Intrado (once a year)
Parse data to GIS tables
Extract data per each PSAP boundary area
Extract and aggregate recent address and road data for all local jurisdictions within each PSAP boundary area
MSAG to GIS Data Comparison
ALI to GIS Data Comparison
Monthly GIS Data Validation Workflow
Quarterly GIS-MSAG-ALI Comparison Workflow
New Mexico 911 (NM911) Program GIS Data Assessment Workflow

## Slide 7: Data Collection
Data Providers were notified via e-mail each month
How: NM911 Data Portal https://portal.nm911.org/
When: 1st – 15th of each month
What: Address points, Road centerlines, and Boundaries
  Accepted data formats: Shapefiles (zipped or unzipped), File geodatabases (zipped)
Notes: If multiple uploads, duplicate data are resolved before data conversion process. Latest data are processed and all other previous uploads will be rejected.

## Slide 8: NM911 Data Portal
Acknowledgement if upload is a Success! No email – We try not to SPAM your inbox!!
As seen in the second half of each month.

## Slide 9: NM911 Data Portal

## Slide 10: NM911 Data Portal

## Slide 11: Data Translation & Conversion
Field Mapping/Crosswalk between local schema to state schema

## Slide 12: Data Translation & Conversion
Data imported to State Schema
Records that doesn’t match the state schema will be exported as import errors feature class and are not included in the state database.

## Slide 13: Coordinate Systems
Local Govt. GIS:
State Plane Coordinate System (SPCS)
State or Regional maps:
UTM Coordinate System
NG911 System uses World Geodetic System (WGS) 1984

## Slide 14: Data Assessment
QA/QC to ensure data integrity
Spatial & Tabular Accuracy Checks
Topology Checks
Data Reviewer Checks & Attribute Rules
Datasets: Road Centerlines, Address Points, Administrative/Addressing Boundary
Fishbone Lines

## Slide 15: Data Assessment
 |  | DATA REVIEWER CHECKS
1 |  | Address Point Address Number Cannot Be 0, Negative, NULL Or Blank
2 |  | Address Point Address Number Should Be Within Road Centerline Address Range
3 |  | Address Point Full Road Name Must Match Road Centerline Full Road Name
4 |  | Address Point Has Invalid Geometry
5 |  | Address Point Must Not Have Duplicate Geometry
6 |  | Address Point Street Name Cannot Be Blank Or NULL
7 |  | NM911 Topology Checks
8 |  | Road Centerline Has Invalid Geometry
9 |  | Road Centerline Left High Address Must Be Odd
10 |  | Road Centerline Left Low Address Is Greater Than Left High Address
11 |  | Road Centerline Left Low Address Must Be Odd
12 |  | Road Centerline Length Must Not Be Less than 15 ft.
13 |  | Road Centerline Must Be Broken And Snapped At Road Intersections
14 |  | Road Centerline Must Not Have Dangles
15 |  | Road Centerline Must Not Have Duplicate Geometry
16 |  | Road Centerline Must Not Have Left Side Overlapping Address Range
17 |  | Road Centerline Must Not Have Right Side Overlapping Address Range
18 |  | Road Centerline Right High Address Must Be Even
19 |  | Road Centerline Right Low Address Is Greater Than Right High Address
20 |  | Road Centerline Right Low Address Must Be Even
21 |  | Road Centerline Should Not Be Multipart

## Slide 16: Data Reporting

## Slide 17: Data Reporting

## Slide 18: Data Correction – Exceptions
Road Centerline Left Low & High Address Must Be Odd
Road Centerline Right Low & High Address Must Be Even
Road Centerline Left Low Address is Greater than Left High Address
Road Centerline Right Low Address is Greater than Right High Address
  Can be marked as Exceptions based on ground conditions
  Exception data column. Mark “Y” or “1” (based on the field data type: TEXT, INTEGER) if there is an exception and leave the column blank if no exception
What are acceptable exceptions?

## Slide 19: Data Correction – Topology
Address Point Must Be Properly Inside the Administrative Boundary
  Administrative Boundary can be replaced with Provisioning/ Addressing Boundary, if available.

## Slide 20: Data Correction - Topology
Roads must be broken and snapped at intersections

## Slide 21: Data Correction – Address Points Examples
Address Point Address Number Cannot Be 0, Negative, Null or Blank
  Ex: 0 JUAN PEREA RD SE

## Slide 22: Data Correction – Address Points Examples
Address Point Address Number Should Be Within Road Centerline Address Range
  Ex: 922 HILLSIDE DR SW

## Slide 23: Data Correction – Road Centerline Examples
Address Point Full Road Name Must Match Road Centerline Full Road Name
  Ex: VALLE VISTA RD NW

## Slide 24: Data Correction – Road Centerline Examples
Road Centerline Must Not Have Right Side Overlapping Address Range
  Ex: SICHLER RD SW

## Slide 25: Fishbone Lines
Visually Compare road centerlines to address points
  Out of numerical order
  On the wrong side of the street
  On the wrong block
  On the wrong side of the city

## Slide 26: Fishbone Analysis
GOOD

## Slide 27: Fishbone Analysis
BAD
Notes: Query data to identify data inaccuracies
Ex: Wrong side of the street or Block: show every fishbone that intersects a street centerline

## Slide 28: Fishbone Analysis
Multiple issues –
Incorrect addressing/ placement
Overlapping address ranges

## Slide 29: Fishbone Analysis – Good or Bad?
Catron County, NM
Notes: Driveways do not intersect. Points are placed on the structure instead of the access point.

## Slide 30: Fishbone Analysis
Notes: Red: Incorrect data. Longer lines indicate more serious error. i.e. valid address points are miles from where they should be

## Slide 31: Fishbone Analysis
Fix: Address range of the road centerline needs to be flipped odd/even

## Slide 32: Address Parity Anomalies

## Slide 33: GIS-MSAG-ALI Comparison
Quarterly Assessments
Essential for Next Generation 911 (NG 9-1-1) data transition
NENA recommends a 98% match rate between the datasets
Data Providers and PSAPs must prioritize to improve data accuracy
Data for Comparison
  GIS – monthly data uploads from GIS Data Providers
  MSAG – quarterly data downloads from Intrado
  ALI – yearly data extract from Lumen (formerly CenturyLink)

## Slide 34: The 9-1-1 Database(s)
MSAG – Master Street Address Guide – Influence and control E9-1-1
ALI – Automated Location Information – Each landline telephone number in a PSAP’s response area is loaded from each serving phone company, scrubbed against the MSAG to obtain ESN and Community information, and loaded into the ALI database. When a 9-1-1 landline call is initiated, the ten digit phone number dips into this database to obtain the location info sent to the PSAP with the voice call
ELT – English Language Translation – a table which translates each ESN to the names of the public safety providers
GIS Data – Geospatial data used to be an “add-on” and is now considered critical to control all or most of the above
GIS Data is CRITICAL for NG911

## Slide 35
A snapshot of MSAG database, Guadalupe County, NM
MSAG Vs GIS Data
A snapshot of Road Centerline attribute table, Guadalupe County, NM

## Slide 36
A snapshot of ALI database for Portales, NM
ALI Vs GIS Data
A snapshot of Address points, Portales, NM

## Slide 37
ESN | POLICE | FIRE | AMBULANCE
869 | HOBBS PD | HOBBS FD | HOBBS EMS
870 | LEA COUNTY SHERIFF | HOBBS FD | HOBBS EMS
870 | LEA COUNTY SHERIFF | HOBBS FD | HOBBS EMS
870 | LEA COUNTY SHERIFF | HOBBS FD | HOBBS EMS
870 | LEA COUNTY SHERIFF | HOBBS FD | HOBBS EMS
871 | LEA COUNTY SHERIFF | KNOWLES FD | LOVINGTON EMS
872 | LEA COUNTY SHERIFF | KNOWLES FD | HOBBS EMS
880 | LEA COUNTY SHERIFF | HOBBS FD | HOBBS EMS
880 | LEA COUNTY SHERIFF | HOBBS FD | HOBBS EMS
881 | LEA COUNTY SHERIFF | KNOWLES FD | LOVINGTON EMS
882 | LEA COUNTY SHERIFF | KNOWLES FD | HOBBS EMS
883 | LEA COUNTY SHERIFF | MONUMENT FD | HOBBS EMS
884 | LOVINGTON PD | LOVINGTON FD | LOVINGTON EMS
885 | LEA COUNTY SHERIFF | LOVINGTON FD | LOVINGTON EMS
886 | LEA COUNTY SHERIFF | TATUM FD | TATUM EMS
887 | LEA COUNTY SHERIFF | MALJAMAR FD | HOBBS EMS
888 | JAL PD | JAL FD | JAL EMS
889 | LEA COUNTY SHERIFF | JAL FD | JAL EMS
890 | EUNICE PD | EUNICE FD | EUNICE EMS
891 | LEA COUNTY SHERIFF | EUNICE FD | EUNICE EMS
892 | TATUM PD | TATUM FD | TATUM EMS
893 | LEA COUNTY SHERIFF | MALJAMAR FD | LOVINGTON EMS
A snapshot of ESNs for Lea County, NM (legacy)
The 9-1-1 Database(s) - ESN
ESNs for Lea County, NM
When a resident calls 9-1-1, the emergency providers dispatched are the same in a given ESN.
In 869, a resident is served by Hobbs Police Dept., Hobbs Fire Dept., and Hobbs EMS

## Slide 38: GIS-MSAG-ALI Comparison
NM911 GIS-MSAG-ALI Synchronization Status Dashboard https://nm911-hub.maps.arcgis.com

## Slide 39: GIS-MSAG-ALI Comparison
Snapshot of Quarterly GIS-MSAG-ALI Comparison Stats, San Juan County – March 2025
MSAG and GIS Datasets used for Comparison
Notes: MSAG Record count – Source Data: 509 and GIS: 506 – eliminated Wireless or VOIP calls rows

## Slide 40: GIS-MSAG Comparison
Road Centerline data compared with MSAG records
Address columns, Community name, and ESN (Concatenated for left and right side of each segment to create unique identifier)
Results are generated in geodatabase and spreadsheet formats
Notes: Address range comparisons were performed on entire road segments and are reported as such. For example, consider a road segment CENTRALAVE|ALBUQUERQUE|00111. In the MSAG, this segment has a low of 100 and a high of 249. In the road centerline file, there are two segments, one with a low of 100 and a high of 149, and another with a low of 200 and a high of 299. In this case, the MSAG segment will report that it does not have the range 250-299. In the road centerline, both segments will report that they are missing the range 150-199.

## Slide 41: GIS-MSAG Comparison – Interpreting Results
REPORT | COMPARISON
Exact MSAG match | 13THMILERD¦FORTSUMNER¦00940
Does not have an MSAG match | ANTELOPERD¦ROSWELL¦00940
Does not have a road centerline match | LYNXRD¦FORTSUMNER¦00940
Not in NM911 road- Rng: 3466-3968 | BILLYTHEKIDDR¦FORTSUMNER¦00942
Not in NM911 road- Val: 3097 | CLAYFLATRD¦FORTSUMNER¦00940
Not in MSAG- Rng: 800-1299, Val: 1499 | EDUNNHL¦FORTSUMNER¦00943
Not in MSAG- Val: 1300 | EFOLEYAVE¦FORTSUMNER¦00943

## Slide 42: MSAG Comparison Report

## Slide 43: GIS-MSAG Comparison – Interpreting Results
BILLYTHEKIDDR|FORTSUMNER|00942 – Not in NM911 road- Rng: 3466-3968
Derived from GIS data (road centerlines)
Derived from MSAG from 911NET
In MSAG data, address range 3466 – 3969 is duplicated for ESN 942 & 943
In GIS data, address range 3466-3968 is part of ESN 943.
Fix: Data Providers & PSAPs must coordinate to establish the authoritative dataset and update the non-authoritative dataset!

## Slide 44: GIS-MSAG Comparison – Interpreting Results
CLAYFLATRD|FORTSUMNER|00940 – Not in NM911 road- Val: 3097
In GIS data, Value 3097 is part of YESO and not in FORT SUMNER. This is valid & No Correction Needed!

## Slide 45: GIS-MSAG Comparison – Interpreting Results
EDUNNHL|FORTSUMNER|00943 – Not in MSAG- Rng: 800-1299, Val: 1499
EDUNNHL|FORTSUMNER|00940 – Does not have a road centerline match
Derived from GIS data (road centerlines)
Derived from MSAG from 911NET
Fix: Data Providers & PSAPs must coordinate to establish the authoritative dataset and update the non-authoritative dataset!

## Slide 46: GIS-ALI Comparison
Tabular ALI data are compared with GIS address point data
If no exact matches found in the addresses then those records will be compared with Road Centerline data to see if the address fits within the address range of the corresponding segment
Address Number, Road Name columns (STR_DIR, STR_PRETYPE, STR_NAME, STR_SUFFIX, POST_DIR), MSAG Community, and ESN

## Slide 47: ALI Comparison Report

## Slide 48: GIS-ALI Comparison – Interpreting Results
Exact NM911 Address Point Match
Address Points Where Clause
  ADD_NUMBER=1115 AND MSAG_COM='FORT SUMNER' AND (ADD_SUFFIX IS NULL or ADD_SUFFIX='') AND (STR_DIR IS NULL or STR_DIR='N') AND STR_NAME_1 = '10TH HL' and ( ESN = '943' OR ESN= '00943')
PHONE_NUMBER | ADD_NUMBER | ADD_SUFFIX | STR_DIR | STR_NAME_1 | COMMUNITY | ESN | DPID
5753552218 | 1115 |  | N | 10TH HL | FORT SUMNER | 00943 | DB_CO

## Slide 49: GIS-ALI Comparison – Interpreting Results
No Match found in NM911 Address Points
Address Point Where Clause:
  ADD_NUMBER=709 AND MSAG_COM='FORT SUMNER' AND (ADD_SUFFIX IS NULL or ADD_SUFFIX='') AND (STR_DIR IS NULL or STR_DIR='N') AND STR_NAME_1 = '2ND ST' and ( ESN = '943' OR ESN= '00943')
Road Centerline Where Clause:
  COMPARE ='N2NDST|FORTSUMNER|00943' AND CAST(HIGH AS INTEGER) >= 709 AND CAST(LOW AS INTEGER) <=709
PHONE_NUMBER | ADD_NUMBER | ADD_SUFFIX | STR_DIR | STR_NAME_1 | COMMUNITY | ESN | DPID
5753557131 | 709 |  | N | 2ND ST | FORT SUMNER | 00943 | DB_CO

## Slide 50: GIS-ALI Comparison – Interpreting Results
No Match found in NM911 Address Points or Road Centerlines
Address Point Where Clause:
  ADD_NUMBER=339 AND MSAG_COM='FORT SUMNER' AND (ADD_SUFFIX IS NULL or ADD_SUFFIX='') AND (STR_DIR IS NULL or STR_DIR='S') AND STR_NAME_1 = '14TH ST' and ( ESN = '941' OR ESN= '00941')
Road Centerline Where Clause:
  COMPARE ='S14THST|FORTSUMNER|00941' AND CAST(HIGH AS INTEGER) >= 339 AND CAST(LOW AS INTEGER) <=339
PHONE_NUMBER | ADD_NUMBER | ADD_SUFFIX | STR_DIR | STR_NAME_1 | COMMUNITY | ESN | DPID
5753556204 | 339 |  | S | 14TH ST | FORT SUMNER | 00941 | DB_CO
PRIORITY!!!

## Slide 51: MSAG Updates: How?
Intrado Integrated User Portal (9-1-1 NET) Portal
You’re not changing the MSAG – you’re submitting a change which must be accepted by Intrado
Intrado then notifies you through the system if the change is accepted
Unaccepted edits may need additional review and verification
9-1-1net.intrado.com

## Slide 52: MSAG Updates: Tools/Functions
MSAG Tools
  MSAG Query
  MSAG Insert
  Query CR
Notes: Glenn – some info from your personal experience will be helpful.

## Slide 53
MSAG Insert
Query Change Request
MSAG Split

## Slide 56: Local Exchange Carrier (LECs) & MSAG Updates
While Lumen (formerly CenturyLink) holds the 9-1-1 Database contract for the state, and contracts with Intrado, there are a dozen or more other phone companies in New Mexico
Each maintains customer service records with valid 9-1-1 addresses
Every time one of those records changes, the local phone company updates its records with Intrado through an SOI (Service Order Input)
These are done every day, and pass all adds/changes/deletes in their systems to Intrado for the 9-1-1 database
Making a change with Intrado does not make a change with the local phone company. And their data will overwrite what’s in the 9-1-1 database, so must be accurate too!

## Slide 57: NM911 ArcGIS Hub
https://nm911-hub.maps.arcgis.com/

## Slide 58: Contact Us
Data/Technical Questions
  Sandeep Talasila
  Earth Data Analysis Center, UNM
  Email: nm911@edac.unm.edu
  Phone: (505) 277-3622 x250
  NM911 Data Portal: Submit a support request
General Questions
  Tyler Fossett
  NM911 GIS Coordinator
  NM Department of Finance & Administration
  Email: Tyler.Fossett@dfa.nm.gov
  Phone: (505) 500-5587